## Slide 1
2.4. Floating Point Numbers
Topics
  IEEE Floating Point Standard
  Rounding
  Floating Point Operations
  Mathematical properties

## Slide 2
IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by Numerical Concerns
  Nice standards for rounding, overflow, underflow
  Hard to make go fast
    Numerical analysts predominated over hardware types in defining standard

## Slide 3
Fractional Binary Numbers
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
bi
bi–1
b2
b1
b0
b–1
b–2
b–3
b–j
• • •
• • •
.
1
2
4
2i–1
2i
• • •
• • •
1/2
1/4
1/8
2–j

## Slide 4
Fractions
Fraction
  X.Y = an-1 bn-1 + an-2 bn-2 + …. + a0 b0 + a-1 b-1 + a-2 b-2 + …
    123.4510 = a2x82 + a1x81 + a0x80 + a-1x8-1 + a-2x8-2 + …
  Separate whole number & fraction
    X = an-1 bn-1 + an-2 bn-2 + …. + a0 b0 => divide by b’s
    0.Y = a-1 b-1 + a-2 b-2 + … => multiply by b’s

## Slide 5
Floating Point Representation
Numerical Form – Scientific Notation (Normalized)
  (–1)s M 2E
    Sign bit s determines whether number is negative or positive
    Significand (Mantissa) M normally a fractional value in range [1.0,2.0).
    Exponent E weights value by power of two
Encoding
  MSB is sign bit
  exp field encodes E
  frac field encodes M
s
exp
frac

## Slide 6
Floating Point Precision
Encoding
  MSB is sign bit
  exp field encodes E
  frac field encodes M
Sizes
  Single precision: 8 exp bits, 23 frac bits
    32 bits total
  Double precision: 11 exp bits, 52 frac bits
    64 bits total
  Extended precision: 15 exp bits, 63 frac bits
    Only found in Intel-compatible machines
    Stored in 80 bits
      1 bit wasted
s
exp
frac

## Slide 7
“Normalized” Numeric Values
Condition
  exp  000…0 and exp  111…1
Exponent coded as biased value
  E = Exp – Bias
    Exp : unsigned value denoted by exp
    Bias : Bias value
      Single precision: 127 (Exp: 1…254, E: -126…127)
      Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
      in general: Bias = 2e-1 - 1, where e is number of exponent bits

## Slide 8
“Normalized” Numeric Values
Significand coded with implied leading 1
  M = 1.xxx…x2
    xxx…x: bits of frac
    Minimum when 000…0 (M = 1.0)
    Maximum when 111…1 (M = 2.0 – )
    Get extra leading bit for “free”

## Slide 9
Examples
FP representation in 5-bit exp, 7-bit frac (sign bit ignored)
1.0101010x2-5
1.1010101x25

## Slide 10
Examples
Binary scientific notation of the fp codes in 5-bit exp & 7-bit frac (sign bit ignored)
01010 0101010
10101 0101010

## Slide 11
exp 2’s E(Biased) 2E
000 0 -2 1/4 (denorms)
001 1 -2 1/4 (norm)
010 2 -1 1/2 (norm)
011 3 0 1 (norm)
100 -4 1 2 (norm)
101 -3 2 4 (norm)
110 -2 3 8 (norm)
111 -1
Exponent coded as biased value
  E = Exp – Bias
    Exp : unsigned value denoted by exp
    Bias : Bias value
      Single precision: 127 (Exp: 1…254, E: -126…127)
      Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
      in general: Bias = 2e-1 - 1, where e is number of exponent bits

## Slide 12
Normalized Encoding Example
Value
  Float F = 15213.0;
  1521310 = 111011011011012 = 1.11011011011012 X 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Floating Point Representation (Class 02):
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
140: 100 0110 0
15213: 1110 1101 1011 01

## Slide 13
“Denormalized” Values
Condition
  exp = 000…0
Value
  Exponent value E = –Bias + 1
  Significand value M = 0.xxx…x2
    xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents value 0
    Note that have distinct values +0 and –0
  exp = 000…0, frac  000…0
    Numbers very close to 0.0
    Lose precision as get smaller
    “Gradual underflow”

## Slide 14
Special Values
Condition
  exp = 111…1
Cases
  exp = 111…1, frac = 000…0
    Represents value(infinity)
    Operation that overflows
    Both positive and negative
    E.g., 1.0/0.0 = 1.0/0.0 = +, 1.0/0.0 = 
  exp = 111…1, frac  000…0
    Not-a-Number (NaN)
    Represents case when no numeric value can be determined
    E.g., sqrt(–1), 

## Slide 15
Summary
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0

## Slide 16
Example -4/3 (exp/frac)
8-bit Floating Point Representation
  the sign bit is in the most significant bit.
  the next four bits are the exponent, with a bias of 7.
  the last three bits are the frac
Same General Form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s
exp
frac
0
2
3
6
7

## Slide 17
Values Related to Exponents
U exp E 2E
0 0000 -6 1/64 (denorms)
1 0001 -6 1/64
2 0010 -5 1/32
3 0011 -4 1/16
4 0100 -3 1/8
5 0101 -2 1/4
6 0110 -1 1/2
7 0111 0 1
8 1000 +1 2
9 1001 +2 4
10 1010 +3 8
11 1011 +4 16
12 1100 +5 32
13 1101 +6 64
14 1110 +7 128
15 1111 n/a (inf, NaN)

## Slide 18
Dynamic Range
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
largest norm
Denormalized
numbers
Normalized
numbers

## Slide 19
Dynamic Range
s exp frac E Value
0 000 00 -2 0
0 000 01 -2 1/4*1/4 = 1/16
0 000 10 -2 2/4*1/4 = 2/16
0 000 11 -2 3/4*1/4 = 3/16
0 001 00 -2 4/4*1/4 = 4/16
0 001 01 -2 5/4*1/4 = 5/16
…
0 010 11 -1 7/4*1/2 = 14/16
0 011 00 0 4/4*1 = 16/16 = 1
0 011 01 0 5/4*1 = 20/16 = 1.25
0 011 10 0 6/4*1 = 24/16 = 1.5
0 011 11 0 7/4*1 = 28/16 = 1.75
0 100 00 1
…
0 110 10 3 6/4*8 = 12
0 110 11 3 7/4*8 = 14
0 111 00 n/a inf
closest to zero
largest denorm
smallest norm
largest norm
Denormalized
numbers
Normalized
numbers

## Slide 20
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
Notice how the distribution gets denser toward zero.
Distribution of Values

## Slide 21
Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} X 2– {126,1022}
  Single  1.4 X 10–45
  Double  4.9 X 10–324
Largest Denormalized 00…00 11…11 (1.0 – ) X 2– {126,1022}
  Single  1.18 X 10–38
  Double  2.2 X 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 X 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ) X 2{127,1023}
  Single  3.4 X 1038
  Double  1.8 X 10308

## Slide 22
Special Properties of Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider -0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 23
An Anedote
Common mistakes of converting a f.p # to an integer
June 4, 1996, a maiden voyage of Ariane 5 Rocket
  $500 M communication satellite on board
  37 sec after liftoff

## Slide 24
An Anedote

## Slide 25
An Anedote
Computer controlling the inertial navigation system sent invalid data to the computer controlling engine nozzles
Instead of flight control info, it sent a diagnostic bit pattern indicating an overflow from 64-bit f.p. to 16-bit integer
Overflow value measured the horizontal velocity of the rocket, which could be more than 5 times higher than that of Ariane 4
Software for Ariane 4 was never to overflow