## Slide 1
Layers of Abstraction
Architecture (instruction set architecture, ISA)
  Highest level of abstraction in computer specification
  The parts of a processor design needed to read and write assembly code
  Concerned about instruction set specification, registers, etc.
Microarchitecture
  Lower-level details about how architecture is implemented
  Concerned about cache sizes, core frequency, etc.
  May contain optimizations (like pipelining, branch prediction) not talked about by architecture
Processor
  Lowest level of abstraction
  Implementation of computer in physical hardware
  Includes materials, circuitry, geometrical arrangements, etc.

## Slide 2
Architecture Design Strategies
CPU Performance formula
  (architecture) (microarch.) (processor)
RISC (Reduced Instruction Set Computer)
  Focus on simple instructions that do 1 thing, lowers
  Fewer instructions, easier to implement, lowers
  But common patterns repeated in code, raises
CISC (Complex Instruction Set Computer)
  Special instructions for common patterns, lowers
  Some instructions do many things at once, raises
  More instructions, harder to implement, raises

## Slide 3
IA32/x86 Processors
Evolutionary Design
  Started in 1978 with 8086 (based on 8-bit 8008 from 1972)
  Layered more features on top as time goes on
  Good:
    Backwards compatibility, still support ALL old features
    Ancient machine code still runs on modern processors
  Bad:
    Old choices no longer relevant
    Obsolete features still wasting space in your computer
Complex Instruction Set Computer (CISC)
  Many different instructions with many different formats
  Hard to match performance of RISC – ARM, MIPS
  But Intel figured out how!

## Slide 5: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32-bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4E 2004 125M 2800-3800
  First 64-bit Intel x86 processor, referred to as x86-64
Core 2 2006 291M 1060-3500
  First multi-core Intel processor
Core i7 2008 731M 1700-3900
  Four cores (our shark machines)

## Slide 6: Intel x86 Processors, cont.

## Slide 7
Intel’s 64-bit Architecture
Tried a radical shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
AMD stepped in with Evolutionary Solution
  x86-64 (now called “AMD64”)
2004: Intel announced EM64T extension
  Extended memory 64-bit technology
  Almost identical to x86-64!
  Still not supported by OS, programmers

## Slide 8
Assembly Programmer’s View
Programmer-Visible State
  EIP (IA32) or RIP (IA64)
    Program Counter (PC)
    Address of next instruction
  Register File
    Heavily used program data
  Condition Codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
CPU
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
A
LU

## Slide 9
Assembly Characteristics
Minimal Data Types
  “Integer” data of 1, 2, or 4 bytes (+ 8 bytes in 64-bit machines)
    Data values
    Addresses (untyped pointers)
  Floating point data of 4, 8, or 10 bytes
  No aggregate types such as arrays or structures
    Just contiguously allocated bytes in memory
Primitive Operations
  Perform arithmetic function on register or memory data
  Transfer data between memory and register
    Load data from memory into register
    Store register data into memory
  Transfer control
    Unconditional jumps to/from procedures
    Conditional branches

## Slide 10
IA32 Machine Basics

## Slide 11: x86-64 Integer Registers
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
%eax
%ebx
%ecx
%edx
%esi
%edi
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
%rsp
%esp

## Slide 12: Data Formats
Word – refers to a 16-bit data type (historically)
  32-bit: double word / “long” word
  64-bit: quad word
In x86-64
              code Suffix size (byte)
  char byte b 1
  short word w 2
  int double l 4
  long quad q 8
  char * quad q 8
  float single prec. s (l) 4
  double double prec. l (q) 8

## Slide 13
Moving Data
Moving Data
  movx Source, Dest:
1st operand => 2nd operand
x refers to the size moved
  q = quad word (64 bits) % rax
  l = long word (32 bits) % eax
  w = word (16 bit) % ax
  b = byte (8 bits) % ah, al
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%ebp
%esp

## Slide 14
Moving Data
Operand Types
  Immediate: Constant integer data
    Like C constant, but prefixed with ‘$’
    E.g., $0x400, $-533
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers (only 8 in 32-bit x86)
    But %rsp and %rbp reserved for special use
    Some others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory
    Various “address modes”

## Slide 15: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest
sw $t0, ($s0)
lw $t0, ($s0)
li $s0,0x400
move $t0, $s0

## Slide 16: Simple Memory Addressing Modes
Direct D Mem[D]
movq X+8, %rax
Normal (indirect) (R) Mem[Reg[R]]
  Register R specifies memory address
  Pointer dereferencing in C movq (%rcx),%rax
Displacement (indexed) D(R) Mem[D+Reg[R]]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 17
Indexed Addressing Modes
Most General Form
  D(Rb,Ri,S) Mem[D + Reg[Rb] + Reg[Ri]*S]
    D: Constant “displacement” 1, 2, or 4 bytes
    Rb: Base register: Any of 8 integer registers
    Ri: Index register: Any, except for %esp
      Unlikely you’d use %ebp, either
    S: Scale: 1, 2, 4, or 8
Special Cases
  (Rb,Ri) Mem[Reg[Rb] + Reg[Ri]]
  D(Rb,Ri) Mem[D + Reg[Rb] + Reg[Ri]]
  (,Ri,S) Mem[Reg[Ri]*s]

## Slide 18
Address Computation Examples
%edx
%ecx
0xf000
0x100
Expression | Computation | Effective Address
0x8(%edx) | 0x8 + 0xf000 | 0xf008
(%edx,%ecx) | 0xf000 + 0x100 | 0xf100
(%edx,%ecx,4) | 0xf000 + 0x100*4 | 0xf400
0x80(,%edx,2) | 0x80 + 0xf000*2 | 0x1e080

## Slide 19
Some Arithmetic Operations
  Format Computation
Two Operand Instructions
  addq Src,Dest Dest = Dest + Src
  subq Src,Dest Dest = Dest – Src MIPS: sub d,r,s (d=r-s)
  imulq Src,Dest Dest = Dest * Src
  salq Src,Dest Dest = Dest << Src Also called shlq
  sarq Src,Dest Dest = Dest >> Src Arithmetic (MIPS: sra)
  shrq Src,Dest Dest = Dest >> Src Logical (MIPS: srl)
  xorq Src,Dest Dest = Dest ^ Src
  andq Src,Dest Dest = Dest & Src
  orq Src,Dest Dest = Dest | Src

## Slide 20
Some Arithmetic Operations
  Format Computation
One Operand Instructions
  incq Dest Dest = Dest + 1
  decq Dest Dest = Dest - 1
  negq Dest Dest = -Dest
  notq Dest Dest = ~Dest

## Slide 21
Addr Computation Instruction
leaq Src, Dest
  Load Effective Address
  Src is address mode expression
  Set Dest to address denoted by expression
Uses
  Computing address without the memory reference
    E.g., translation of p = &x[i];
  Similar to MIPS ‘la’ instruction
  Can also be (ab)used for computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8.

## Slide 22
Using leaq for Arithmetic
leaq (%rdx,%rdx,2),%rdx
# %rdx = 3*%rdx
What is the result (stored in %rdx)?
movq (%rdx,%rdx,2),%rdx
# %rdx = Memory[3*rdx]

## Slide 23: Arithmetic Expression Example
Carnegie Mellon
long arith
(long x, long y, long z)
{
long t1 = x + y;
long t2 = z + t1;
long t3 = x + 4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5

## Slide 24: Arithmetic Expression Example
Carnegie Mellon
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication (slow!)
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x + y;
long t2 = z + t1;
long t3 = x + 4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2),%rdx # rdx=3*y
salq $4, %rdx # rdx=16*(3*y)
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret
x = %rdi; y = %rsi; z = %rdx

## Slide 25: Zero/sign extension
Carnegie Mellon
movzSR s,r
  Move with zero extension
  %dl = AA; movzbq %dl, %rax
    %rax = 0000 0000 0000 00AA
movsSR s,r
  Move with sign extension
  %dl = AA; movsbq %dl, %rax
    %rax = FFFF FFFF FFFF FFAA
cltq (Convert Long To Quad)
  sign extend %eax to %rax (only for %eax & %rax)

## Slide 26: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 27: Procedure calls in x86
Arguments
  %rdi, %rsi, %rdx, %rcx, %r8, %r9
Return value
  %rax
Return Address - Stack-based

## Slide 28: Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 29: Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 30: Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 31: Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 32: Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 33: Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address