## Slide 1
Combinational logic
  No memory, stateless
  A set of inputs uniquely and unambiguously specifies what outputs are
  Use Boolean logic (combinations of true and false)
4.2. Logic Design

## Slide 2
Combinational logic
  No memory, stateless
  A set of inputs uniquely and unambiguously specifies what outputs are
  Use Boolean logic (combinations of true and false)
4.2. Logic Design

## Slide 3: Bit Equality
  Generate 1 if a and b are equal
Bit equal
a
b
eq
eq = (a&&b)||(!a&&!b)

## Slide 4: Bit Equality
  Generate 1 if a and b are equal
        eq = a’&b’ + a&b
Bit equal
a
b
eq
eq = (a&&b)||(!a&&!b)
a | b | eq
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5: Word Equality
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 6: Bit-Level Multiplexor
  multiplexor (mux), selector
    Control signal s
    Data signals a and b
    Output a when s=1, b when s=0
Bit MUX
b
s
a
out
out = (s&&a)||(!s&&b)
HCL Expression
Mux
s

## Slide 7
s | a | b | o
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Mux
s

## Slide 8: Word Multiplexor
  Select input word A or B depending on control signal s
Word-Level Representation
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 9
Input a,b enables one of 4 outputs
  a,b = 00 -> out0
  a,b = 01 -> out1
  a,b = 10 -> out2
  a,b = 11 -> out3
a
b
Out0
Out1
Out2
Out3
Decoder

## Slide 10
a
b
Out0
Out1
Out2
Out3
a | b | Out0 | Out1 | Out2 | out3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Out0 = a’b’
Out1= a’b
Out2 = ab’
Out3 = ab

## Slide 11
a
b
Carry-out
Carry-in
sum
1-bit Adder: Properties
  Three inputs: a, b, Carry-in
  Two outputs: sum, C-out
1-bit Adder

## Slide 12
a
b
Carry-out
Carry-in
sum
1-bit Adder: Properties
  Three inputs: a, b, Carry-in
  Two outputs: sum, C-out
1-bit Adder
  a b Cin S Cout
  0 0 0 0 0
  0 0 1 1 0
  0 1 0 1 0
  0 1 1 0 1
  0 0 1 0
  1 0 1 0 1
  1 1 0 0 1
  1 1 1 1 1

## Slide 13
  Carry-Out implementation
  Cout =(b ⋅ Cin) + (a ⋅ Cin) + (a⋅b)
  Similar implementation of Sum

## Slide 14
1-bit ALU
1-bit ALU
  1-bit adder
  Logical unit:
  and/or

## Slide 15
1-bit ALU
Capable of
ADD, AND, and OR
How to add SUB ?
  a – b = a + (~b + 1)

## Slide 16
1-bit ALU
Capable of
ADD, AND, and OR
How to add SUB ?
  a – b = a + (~b + 1)
  Add Binvert
  How to add 1 ?

## Slide 17
ADD, AND, OR, SUB
How to add NOR ?
  (A+B)’ = A’B’
  (AB)’ = A’ + B’
  a-b
  -a+b
  -a-b = -(a+b)
  a+b
1-bit ALU

## Slide 18
CarryIn
ALU0
CarryOut
CarryIn
Operation
a0
b0
Result0
CarryIn
ALU1
CarryOut
a1
b1
Result1
CarryIn
ALU2
CarryOut
a2
b2
Result2
CarryIn
ALU 31
CarryOut
a31
b31
Result31



From 1-bit ALU to
32-bit ALU
  Chain carry-out to carry-in to the next bit
  Set CarryIn in the least significant bit to 1 for subtraction
32-bit ALU