## Slide 1
Machine Org. from Building Blocks
PC
Registers
CPU
Memory
Object Code
Program Data
Stack
OS Data/Code
Addresses
Data
Instructions
Condition
Codes
ALU

## Slide 2
Machine Org. from Building Blocks
PC
Registers
CPU
Memory
Object Code
Program Data
Stack
OS Data/Code
Addresses
Data
Instructions
Condition
Codes
ALU

## Slide 3
Machine Org. from Building Blocks
PC
Registers
CPU
Memory
Object Code
Program Data
Stack
OS Data/Code
Addresses
Data
Instructions
Condition
Codes
ALU
Given a program in Memory, how does silicon execute each instruction (machine code) ?

## Slide 4: Instruction Decoding
Instruction Format
  Instruction byte icode:ifun
  Optional register byte rA:rB
  Optional constant word valC
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional

## Slide 5: Instruction Decoding
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional
Given an instruction (machine code), how does Silicon tell which building blocks to use and HOW?

## Slide 6: How to design to handle these instr?
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB),rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6
addq
6
0
subq
6
1
andq
6
2
xorq
6
3
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 7: How to design machine ?
Create a neutral machine good for any instruction in whichever order
Given a neutral machine
  Store program in memory
  Bring one instruction at a time, and execute it
  Move on to the next instruction (except for jump and call)
Stored Program Computer
  Von Neumann, 1945
  Computer re-usable for any programs
jXX Dest
call Dest
irmovq V, rB
rmmovq rA, D(rB)
mrmovq D(rB), rA
cmovXX rA, rB
OPq rA, rB
ret
pushq rA
popq rA

## Slide 8: Five steps of instruction execution
Bring a new machine code from memory to IR (instruction register)
Check i-code
    Get rA, rB, valC, if used
Compute via ALU
    OP
    valB+D
    %rsp+-8
Get memory data
Store result in register
    write data
Update PC
jXX Dest
call Dest
irmovq V, rB
rmmovq rA, D(rB)
mrmovq D(rB), rA
cmovXX rA, rB
OPq rA, rB
ret
pushq rA
popq rA

## Slide 9: Five steps of instruction execution
Bring a new machine code from memory to IR
  iCode, iFun, rA, rB, valC
  PC + # -> valP
Check i-code
  R[rA] -> valA, R[rB] -> valB
Compute via ALU
  {OP, valB+D, %rsp+-8} -> valE
Get memory data
  valM
Store result in register
Update PC
  {valP, target addr, valM} -> PC
jXX Dest
call Dest
irmovq V, rB
rmmovq rA, D(rB)
mrmovq D(rB), rA
cmovXX rA, rB
OPq rA, rB
ret
pushq rA
popq rA
5
0
rA
rB
V

## Slide 10: Five steps of instruction execution
Bring a new machine code from memory to IR
  iCode, iFun, rA, rB, valC
  PC + # -> valP
Check i-code
  R[rA] -> valA, R[rB] -> valB
Compute via ALU
  {OP, valB+D, %rsp+-8} -> valE
Get memory data
  valM
Store result in register
Update PC
  {valP, target addr, valM} -> PC
jXX Dest
call Dest
irmovq V, rB
rmmovq rA, D(rB)
mrmovq D(rB), rA
cmovXX rA, rB
OPq rA, rB
ret
pushq rA
popq rA
5
0
rA
rB
V
Fetch
Decode
Execute
Memory
Write Back

## Slide 11: 5-cycle SEQ
Fetch
  Read instruction from instruction memory
Decode
  Read registers
Execute (ALU op)
  Compute value or address
Memory
  Read or write data
Write Back (Reg WB)
  Write registers
PC
  Update program counter
Building Blocks

## Slide 12: Multiplexor (Selector)
Select input word A or B depending on control signal s
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
Out = [s: A; 1: B;];
s
B
A
Out
MUX

## Slide 13: 5-cycle SEQ
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 14: 5-cycle SEQ
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 15: SEQ Hardware
Key
Blue boxes: predesigned hardware blocks
  E.g., memories, ALU
Gray boxes: control logic
White ovals: labels for signals
Thick lines: 64-bit word values
Thin lines: 4-8 bit values
Dotted lines: 1-bit values

## Slide 16: Computed Values - Variables
Memory
  valM Value from memory
Execute
  valE ALU result
  Cnd Branch/move flag
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
valB Register value B
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC

## Slide 17: Move Operations
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 18: irmovq V, rB
Fetch
  valC <- V
via ALU
ALU_A <- valC; ALU_B <- 0; Add; valE
Transfer
dstE <- rB; valE <- valE, write

## Slide 19: rmmovq rA, D(rB)
Fetch
valC <- D;
Decode
  valA <- R[rA]; valB <- R[rB]
Add
  ALU_A <- valC; ALU_B <- valB; add;valE
3. Memory Write
M_addr <- valE; M_data <- valA; M_write

## Slide 20: Stage Computation: rmmovq
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
Decode
Execute
Memory
Write
back
PC update

## Slide 21: Stage Computation: rmmovq
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
Execute
Memory
Write
back
PC update

## Slide 22: Stage Computation: rmmovq
  Use ALU for address computation
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
Memory
Write
back
PC update

## Slide 23: Stage Computation: rmmovq
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC update

## Slide 24: Stage Computation: rmmovq
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC <- valP
PC update
Update PC

## Slide 25: Executing Arith./Logical Operation
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  Perform operation
  Set condition codes
Memory
  Do nothing
Write back
  Update register
PC Update
  Increment PC by 2
OPq rA, rB
6
fn
rA
rB

## Slide 26: Stage Computation: Arith/Log. Ops
  Formulate instruction execution as sequence of simple steps
  Use same general form for all instructions
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 27: Executing popq
Fetch
  Read 2 bytes
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Write result to register
PC Update
  Increment PC by 2
popq rA
b
0
rA
8

## Slide 28: Stage Computation: popq
  Use ALU to increment stack pointer
  Must update two registers
    Popped value
    New stack pointer
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R[%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 29: Executing Conditional Moves
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  If !cnd, then set destination register to 0xF
Memory
  Do nothing
Write back
  Update register (or not)
PC Update
  Increment PC by 2
cmovXX rA, rB
2
fn
rA
rB

## Slide 30: Stage Computation: Cond. Move
  Read register rA and pass through ALU
  Cancel move by setting destination register to 0xF
    If condition codes & move condition indicate no move
cmovXX rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  0
Decode
Read operand A
valE  valB + valA
If ! Cond(CC,ifun) rB  0xF
Execute
Pass valA through ALU
(Disable register update)
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 31: Executing Jumps
Fetch
  Read 9 bytes
  Increment PC by 9
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 32: Stage Computation: Jumps
  Compute both addresses
  Choose based on setting of condition codes and branch condition
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Cnd  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Cnd ? valC : valP
PC update
Update PC

## Slide 33: Executing call
Fetch
  Read 9 bytes
  Increment PC by 9
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 8
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 34: Stage Computation: call
  Use ALU to decrement stack pointer
  Store incremented PC
call Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%rsp]
Decode
Read stack pointer
valE  valB + –8
Execute
Decrement stack pointer
M8[valE]  valP
Memory
Write return value on stack
R[%rsp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 35: Executing ret
Fetch
  Read 1 byte
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 36: Stage Computation: ret
  Use ALU to increment stack pointer
  Read return address from memory
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%rsp]
valB  R[%rsp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read return address
R[%rsp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address