## Slide 1: x86 Encoding

## Slide 2: x86 Encoding

## Slide 3: x86 Encoding

## Slide 4
Object Code
Setup
  Label .L49 becomes address 0x804875c
  Label .L57 becomes address 0x8048bc0
08048718 <unparse_symbol>:
8048718: 55 pushl %ebp
8048719: 89 e5 movl %esp,%ebp
804871b: 8b 45 08 movl 0x8(%ebp),%eax
804871e: 83 f8 05 cmpl $0x5,%eax
8048721: 77 39 ja 804875c <unparse_symbol+0x44>
8048723: ff 24 85 c0 8b jmp *0x8048bc0(,%eax,4)

## Slide 7
Object Code
89 e5 movl %esp,%ebp
  Opcode: 89
  modRM (mod R/M reg)
  11 100 (esp) 101 (ebp)
08048718 <unparse_symbol>:
8048718: 55 pushl %ebp
8048719: 89 e5 movl %esp,%ebp
804871b: 8b 45 08 movl 0x8(%ebp),%eax
804871e: 83 f8 05 cmpl $0x5,%eax
8048721: 77 39 ja 804875c <unparse_symbol+0x44>
8048723: ff 24 85 c0 8b jmp *0x8048bc0(,%eax,4)

## Slide 8
Object Code
8b 45 08 movl 0x8(%ebp),eax
  Opcode: 8b
  modRM (mod R/M reg)
  01 000 (eax) 101 (ebp)
08048718 <unparse_symbol>:
8048718: 55 pushl %ebp
8048719: 89 e5 movl %esp,%ebp
804871b: 8b 45 08 movl 0x8(%ebp),%eax
804871e: 83 f8 05 cmpl $0x5,%eax
8048721: 77 39 ja 804875c <unparse_symbol+0x44>
8048723: ff 24 85 c0 8b jmp *0x8048bc0(,%eax,4)

## Slide 9: Y86-64 Instructions
Format
  1–10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 10: Y86-64 Instruction Set #1
Byte
A
0
rA
F
jXX Dest
7
fn
Dest
B
0
rA
F
call Dest
8
0
Dest
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
6
fn
rA
rB
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
cmovXX rA, rB
OPq rA, rB
ret
pushq rA
popq rA

## Slide 11: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 12: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 13: Y86-64 Instruction Set
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB),rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6
addq
6
0
subq
6
1
andq
6
2
xorq
6
3
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 14: Y86-64 Processor State
ZF
SF
OF
  Program Registers
    15 registers (omit %r15). Each 64 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 15: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 16: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86-64 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 17: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 18: Move Operations
  Like the x86-64 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D
rA
rB

## Slide 19: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 f2 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:
$0xabcd: 00 00 00 00 00 00 ab cd

## Slide 20: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovq instruction
    (Conditionally) copy value from source to destination register
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 21: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 22: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 23: Y86-64 Program Stack
  Region of memory holding program data
  Used in Y86-64 (and x86-64) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 24: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 25: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 26: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  x86-64 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 27: Y86 Code Generation Example
x86 Code
Y86 Code
len2:
pushq %rbp
movq %rsp,%rbp
xorq %rcx,%rcx
movq 8(%rbp),%rdx
movq (%rdx),%rax
jmp .L26
len2:
pushq %rbp # Save %ebp
rrmovq %4sp,%rbp # Set frame
xorq %rcx,%rcx # len = 0
mrmovq 8(%rbp),%rdx # Get a
mrmovq (%rdx),%rax # Get *a
jmp .L26 # Goto entry

## Slide 28: Y86 Code Generation Example
x86 Code
  Loop + Finish
Y86 Code
  Loop + Finish
L24:
movq (%rdx),%rax
incq %rcx
L26:
addq $4,%rdx
testq %rax,%rax
jne L24
movq %rbp,%rsp
movq %rcx,%rax
popq %rbp
ret
L24:
mrmovq (%rdx),%rax # Get *a
irmovq $1,%rsi
addq %rsi,%rcx # len++
L26: # Entry:
irmovq $4,%rsi
addq %rsi,%rdx # a++
andq %rax,%rax # *a == 0?
jne L24 # No--Loop
rrmovq %rbp,%rsp # Pop
rrmovq %rcx,%rax # Rtn len
popq %rbp
ret